## Slide 1: Inferential Analysis: Correlation Matrix
Strong Positive Relationships between:
Torque and Flow Meter 1, Torque and Flow Meter 2, RPM and Flow Meter 1, Torque and RPM
Strong Negative Relationships between:
Flow Meter Daily Torque, Torque and Maximum Daily Torque, Tube Pressure and Maximum Daily Torque, Tube Pressure and pump failure and Maximum Daily Torque, Flow Meter 1 and Tube Pressure, Flow Meter 2 and Tube Pressure, RPM and Maximum
Corelation | SURJEK_FLOW_METER_1 | SURJEK_FLOW_METER_2 | ROTATIONAL_PUMP_RPM | SURJEK_PUMP_TORQUE | MAXIMUM_DAILY_PUMP_TORQUE | SURJEK_TUBE_PRESSURE
SURJEK_FLOW_METER_1 | 1.00 |  |  |  |  | 
SURJEK_FLOW_METER_2 | 0.66 | 1.00 |  |  |  | 
ROTATIONAL_PUMP_RPM | 0.77 | 0.61 | 1.00 |  |  | 
SURJEK_PUMP_TORQUE | 0.80 | 0.48 | 0.74 | 1.00 |  | 
MAXIMUM_DAILY_PUMP_TORQUE | 0.05 | 0.17 | -0.02 | 0.04 | 1.00 | 
SURJEK_TUBE_PRESSURE | 0.04 | 0.05 | 0.06 | 0.05 | 0.16 | 1.00
PUMP FAILURE (1 or 0) | 0.50 | 0.33 | 0.42 | 0.45 | 0.11 | 0.01

## Slide 2: Inferential Analysis: Correlation Matrix for Rolling Standard Deviation
Strong Positive Relationships between:
Torque and Flow Meter 1, Maximum Daily Torque and Flow Meter 2, Pump Failure and Flow Meter 2, Torque and Pump Failure
Strong Negative Relationships between:
Flow Meter 1 and Tube Pressure, Flow Meter 1 and Efficiency, Flow Meter 2 and Tube Pressure, RPM and Pressure, RPM and Efficiency, Torque and Pressure, Torque and Efficiency, Tube Pressure and Maximum Daily Torque, Efficiency and Maximum Daily Torque, Pressure and Efficiency, Pressure and Pump failure, Efficiency and Pump Failure
Corelation | SURJEK_FLOW_METER_1 | SURJEK_FLOW_METER_2 | ROTATIONAL_PUMP_RPM | SURJEK_PUMP_TORQUE | MAXIMUM_DAILY_PUMP_TORQUE | SURJEK_TUBE_PRESSURE | SURJEK_ESTIMATED_EFFICIENCY | PUMP FAILURE (1 or 0)
SURJEK_FLOW_METER_1 | 1.00 |  |  |  |  |  |  | 
SURJEK_FLOW_METER_2 | 0.09 | 1.00 |  |  |  |  |  | 
ROTATIONAL_PUMP_RPM | 0.25 | 0.16 | 1.00 |  |  |  |  | 
SURJEK_PUMP_TORQUE | 0.59 | 0.41 | 0.41 | 1.00 |  |  |  | 
MAXIMUM_DAILY_PUMP_TORQUE | 0.15 | 0.52 | 0.30 | 0.46 | 1.00 |  |  | 
SURJEK_TUBE_PRESSURE | -0.01 | -0.07 | -0.01 | -0.03 | -0.01 | 1.00 |  | 
SURJEK_ESTIMATED_EFFICIENCY | -0.10 | 0.10 | -0.01 | -0.06 | -0.19 | -0.15 | 1.00 | 
PUMP FAILURE (1 or 0) | 0.21 | 0.61 | 0.38 | 0.54 | 0.55 | -0.02 | -0.07 | 1.00

## Slide 3: Rolling SD Corelation Plot wrt PUMP FAILURE
Pump failure is correlated with Flow meter 2, Daily Pump Torque, Torque, RPM
And Negatively correlated with Tube Pressure and Efficieny
Chart: 
| SURJEK_FLOW_METER_2 | MAXIMUM_DAILY_PUMP_TORQUE | SURJEK_PUMP_TORQUE | ROTATIONAL_PUMP_RPM | SURJEK_FLOW_METER_1 | SURJEK_TUBE_PRESSURE | SURJEK_ESTIMATED_EFFICIENCY
 | 0.61128 | 0.55329 | 0.53529 | 0.38226 | 0.21342 | -0.020523 | -0.069861

## Slide 4: Regression Equartion wrt Pump Failure
Chart: 

## Slide 5: Conclusion
Regression:
ROTATIONAL_PUMP_RPM is mostly coefficiently related to Pump Failure
Correlation:
SURJEK_FLOW_METER2 is most positive correlated to Pump Failure